## Slide 1: Hidden Layer Prediction
William Huibregtse
whuibreg@iu.edu

## Slide 2: Algorithm Overview
Input is a vector containing m values
A supplied n x m weights matrix represents the weights for each node in a network
Activations at each node are calculated using matrix multiplication and the Rectified Linear Units (ReLu)
These outputs are streamed out

## Slide 3: Algorithm Applications
Input and Output vector sizes can be different, so this could be used for transforming inputs into a new vector space
Time-sensitive (e.g. financial) network predictions as input stream could be IP Stream
Large-batch network weight learning due to speed of calculations

## Slide 4: Input Data Choreography
Input is vector of floating point values
8 bit exponent, 24 bit mantissa
Vector size (M) passed to Kernel
N x M weights matrix passed to Kernel

## Slide 5: Output Data Choreography
Stream of activations vectors containing N floating points
Activation output determined using Rectified Linear Units (ReLu) activation function

## Slide 6: Expected Performance Gain
Much faster execution than a ControlFlow implementation, especially when the input data arrives via IP Stream
Multiple Kernels could be chained together to create a multilayer perceptron
Output for one vector takes approximately 49 ticks @ estimated 200 MHz or 245 pico-seconds for calculated activation